## Slide 1: The Drumming Robot
Michael Engstrom
~
ECE 579 – Winter 2013

## Slide 2: Adding to ‘DIM’ Robot

## Slide 3: Project Idea
Design a robot that will play drums in rhythm to an audio source which is detected in the environment
A robot control board will move servos to make arms and legs pound drums to a beat
An input device will detect the audio, extract the beat, and send the information to the robot controller

## Slide 4: Project Phases
Mechanical design of robot
  Arms and legs to beat drums
  Interface to control software
Software
  Input of audio source
  Beat detection
  Output to robot controller

## Slide 5: Mechanical Design
Add limbs to the DIM robot (as seen in the Robot Theater window)
Use servos to move limbs
A Pololu ‘Orangutan SVP’ robot controller will handle the servo movement

## Slide 6: The Pololu Orangutan SVP Servo Controller

## Slide 7: Orangutan SVP from Pololu

## Slide 8: Orangutan Specifications

## Slide 9: DIM’s Torso and Arm

## Slide 10: Software Design
Beat Detection Algorithm
  Rice University Project
  Based on an MIT design
  Uses MATLAB to extract beat information from audio input
Serial interface to Orangutan board
  BPM and control information

## Slide 11: Beat Detection

## Slide 12: PSYCHOACOUSTIC SIMPLIFICATION
Simplification of Noise sources

## Slide 14: Beat Detection Algorithm
Step 1 – Frequency Filterbank
  Split audio file into several frequency ranges
    Similar instrument ranges can inhibit the detection of the beat
  Allows for different instruments to be detected
    0-200Hz, 200-400Hz, 400-800Hz, 800-1600Hz, 1600-3200Hz

## Slide 15: Beat Detection Algorithm
Step 1 – Frequency Filterbank
Each filter is implemented using a sixth-order elliptic filter
  3 dB of ripple in the passband
  40 dB of rejection in the stopband.

## Slide 16: Beat Detection Algorithm
Step 1 – Frequency Filterbank

## Slide 17: Beat Detection Algorithm
Step 1 – Frequency Filterbank

## Slide 18: Beat Detection Algorithm
Step 2 – Envelope Smoothing
  Low-Pass Filter each of the signal segments
    Convert to Frequency Domain
    Convolve and transform signal
  Allows for detection of sudden changes in audio content

## Slide 19: Beat Detection Algorithm
Step 2 – Envelope Smoothing: Example

## Slide 20: Beat Detection Algorithm
Step 2 – Envelope Smoothing: Example

## Slide 21: Beat Detection Algorithm
Step 3 – Differentiate signal
  Accentuate when the sound changes
  Corresponds to beats
Step 4 – Rectify signal
  Only see changes in sound
  Signals ready to be analyzed

## Slide 22: Beat Detection Algorithm
Step 5 – Comb Filter
  Use various filters
  Determine which has highest energy
  Maximum value is the fundamental tempo

## Slide 23: Beat Detection Algorithm
A Comb Filter is used to find tempo maxima
  For delay T and gain α the magnitude response is
Local maxima are wherever is near 1 at the Tth roots of unity, expressed as

## Slide 24: Beat Detection Algorithm
Stimulate a comb filter with delay T and gain α with a right-sided pulse train of height A and period k
We get reinforcement (resonance) if T=k .
Let and be the input and output signals at time t
then = + (1-α)

## Slide 25: Beat Detection Algorithm
Energy is higher at dominant tempos

## Slide 26: Implementing in MATLAB
Input audio from .wav file or microphone
  Extract BPM information
    Algorithm described previously
Send data to Orangutan robot controller
  Serial interface between host and controller
  Change speed and tempo of robot drumming arms according to inputs

## Slide 27: MATLAB Plots

## Slide 28: Smoothing Plot

## Slide 29: Differentiate and Rectify

## Slide 30: Comb Filter

## Slide 31: The Drumming Robot

## Slide 32: References
Balanço: The Contour of Relative Offbeatness
  Mehmet Vurkaç - 2012
Beat Sync Project – Rice University 2001
  http://www.clear.rice.edu/elec301/Projects01/beat_sync/
Pololu Robotics and Electronics
  http://www.pololu.com