## Slide 1: Audio Beat Detection with Application to Robot Drumming
~
Michael Engstrom

## Slide 2: Drumming Robot & Robot Drum

## Slide 3: Beat Detection Goals
Design a robot that will play drums in rhythm to an audio source which is detected in the environment
A robot control board will move servos to make arms and legs pound drums to a beat
An input device will detect the audio, extract the beat, and send the information to the robot controller

## Slide 4: Beat Detection Phases
Software Design
  Input of audio source
  Beat detection
  Output to robot controller
Mechanical Design
  Arms and legs to beat drums
  Interface to control software

## Slide 5: Beat Detection
Tempo is complex
  Counterpoint, grouping, hierarchy are subtly combined and interpreted by the human ear
Beat (or pulse) is simpler
  The sense of equally spaced temporal units (Handel, 1989)
  Detection using frequency decomposition
    Fourier Transforms can detect frequency power trends to determine the beat of an audio sample
Notes: Add video and pictures early to show what I am working with… Done!

## Slide 6: Beat Detection
Audio input samples can be decomposed
Eric Scheirer developed a BPM Detection Algorithm in 1989
Algorithm steps:
  Frequency Filterbank
  Envelope Extraction (Fourier Transform)
  Differentiation
  Rectification
  Comb Filter (to match sample to known bpm)
Notes: Name algorithm author

## Slide 7: Drumming Robot in Action

## Slide 9: Beat Detection Algorithm
Step 1 – Frequency Filterbank
  Split audio file into several frequency ranges
    Similar instrument ranges can inhibit the detection of the beat
  Allows for different instruments to be detected
    0-200Hz, 200-400Hz, 400-800Hz, 800-1600Hz, 1600-3200Hz

## Slide 10: Beat Detection Algorithm
Step 1 – Frequency Filterbank
Each filter is implemented using a sixth-order elliptic filter
  3 dB of ripple in the passband
  40 dB of rejection in the stopband.

## Slide 11: Beat Detection Algorithm
A Butterworth lowpass filter command in MATLAB
  [n, Wn] = buttord(Wp,Ws,Rp,Rs)
    Wp: Passband corner (cutoff) frequency
    Ws: Stopband corner frequency
    Rp: Passband ripple
    Rs: Stopband attenuation
  Returns
    n: Lowest filter order (as integer scalar)
    Wn: Cutoff frequencies (as scalar or vector)

## Slide 12: Beat Detection Algorithm
Step 1 – Frequency Filterbank

## Slide 13: Beat Detection Algorithm
Step 1 – Frequency Filterbank

## Slide 14: Fourier Transforms
  Convert a signal from Time to Frequency Domain
    Separates frequency and magnitude components

## Slide 15: Fourier Transforms
  Convert a signal from Time to Frequency Domain
    Separates frequency and magnitude components
  Fourier Transform Pair:
    Note that the algorithm completes after multiplying the Frequency Domain signal and does not need to convert the signal to the Time Domain after this operation.

## Slide 16: Fourier Transforms
  Convert a signal from Time to Frequency Domain
    Separates frequency and magnitude components
  The Discrete Fourier Transform for digital signals:
  The number of samples N affects calculation speed
    Larger number of samples increases accuracy but also increases calculation time
    Parameterization of values helped determine the best tradeoff of speed and accuracy

## Slide 17: Beat Detection Algorithm
Step 2 – Envelope Extractor
  Filter each of the signal segments
  Convert to Frequency Domain using FFT or DFT
  Convolve and transform signal
  Multiplication in Frequency Domain is the same as Convolution in the Time Domain

## Slide 18: Beat Detection Algorithm
Step 2 – Envelope Extractor: 1.5s sample
  Input signal is noisy and duplicates information

## Slide 19: Beat Detection Algorithm
Step 2 – Envelope Extractor: 1.5s sample
  Signal shape is retained and noise is removed

## Slide 20: Beat Detection Algorithm
Step 2 – Windowing with Hanning Window
Signals which have components outside the sampling range of Fourier Transform operations can cause ‘leakage’
Leakage affects the accuracy of the signal representation in the Frequency Domain
Applying a bandpass filter to the signal before performing the transform improves the result of the operation

## Slide 21: Beat Detection Algorithm
Step 2 – Windowing with Hanning Window as shown in the equation by
where n = bin number (for Spectrum analyzer equipment the number of bins is the granularity of frequency representation) and N = number of bins (number of slices displayed on a screen). (Source: Witte)

## Slide 22
An input signal is multiplied with a Hamming Window
(Source: Witte)
Notes: Add slides for input signal with leakage and how windowing improves. Done

## Slide 23
The signal is tapered to zero as each end is approached.
Transients will not be introduced with the windowed signal during the FFT algorithm
(Source: Witte)
Notes: Add slides for input signal with leakage and how windowing improves

## Slide 24: Beat Detection Algorithm
Below is an FFT of a signal with spectral leakage present. The detected frequency magnitude is reduced and spread out.
(Source: Witte)
Notes: Add slides for input signal with leakage and how windowing improves

## Slide 25: Beat Detection Algorithm
Below is an FFT of a windowed signal. The detected frequency magnitude is higher and there are no diffused frequency elements.
(Source: Witte)

## Slide 26: Beat Detection Algorithm
Steps 3 & 4 combined in one MATLAB module
  Step 3 – Differentiate signal
    Accentuate when the sound changes
    Corresponds to beats
  Step 4 – Rectify signal
    Only see changes in sound
    Signals ready to be analyze
  Example on next slide from MATLAB

## Slide 27
Half-wave rectified signal retains positive values
Notes: Add original signal to compare what this effect is

## Slide 28: Beat Detection Algorithm
Step 5 – Comb Filter
  Use various filters
  Determine which has highest energy
  Maximum value is the fundamental tempo

## Slide 29: Beat Detection Algorithm
A Comb Filter is used to find tempo maxima
  For delay T and gain α the magnitude response is
When multiplying the FFT result with a comb filter, local maxima are found wherever is near 1
Multiplying a Comb Filter and the DFT of the input signal is key to the Beat Detection Algorithm

## Slide 30: Beat Detection Algorithm
A signal at 150BPM below shows energy also at the 75BPM octave

## Slide 31: Software Design – Host Side
MATLAB Software Functionality:
  Input audio from file or microphone
    .wav file or 10 seconds of microphone sample
  Follow Scheirer Algorithm in Matlab
    Find FFT of input signal and multiply with Comb Filters of known BPM
    Keep highest multiplied output value, discard others
    Result is BPM value
  Send BPM control value using Serial connection to Robot Controller
Notes: Clarify algorithm name and author. Maybe have a version of this slide near the beginning of presentation.

## Slide 32: Host Side BPM Detection

## Slide 33: Robot Design
The serial control signal is sent to robot controller for the ‘DIM’ robot arm movement

## Slide 34: Robot - Mechanical Design
Added limbs to the DIM robot (as seen in the Robot Theater window)
Servo motors utilized for motion of arms and shoulders
Implemented Pololu ‘Orangutan SVP’ robot controller for servo movement

## Slide 35: Robot - Mechanical Design
Arms and legs to beat drums
  Constructed of lamps, casters and servos
  Allowed for 3 degrees of freedom per arm
Drumming arms attached to ‘DIM’ robot torso
  Shoulder and elbow movement simulates humanoid range and motion while drumming

## Slide 36: Robot - Mechanical Design

## Slide 37: Robot - Mechanical Design
Arms
  Lamp arms purchased from thrift store
  Offset servo moves arm indirectly (not at joint)

## Slide 38: Robot - Mechanical Design
Arms
  Shoulder made from caster with wheel removed and servos mounted (side to side motion shown).

## Slide 39: Robot - Mechanical Design
Arms
  Close-up of shoulder up and down motion

## Slide 40: Robot - Mechanical Design
Completed Arms
  Mounted on Robot torso

## Slide 41: Robot – Hardware Controller Design
Serial interface to Orangutan board
  Pololu robot controller
  Receives BPM and control information from Host
  Can also be controlled by on board buttons
Output is drumming movement in time with BPM using servos to move robot arms
  Robot Controller changes BPM of drumming every time new serial BPM data is received from host

## Slide 42: Robot – Hardware Controller Design
Software
  Pololu Robot Controller
    Interface to control software
    Input Serial BPM data
    Move robot limbs to drum at BPM
Next are some details regarding servos and the Orangutan Robot Controller

## Slide 43: A closeup view of the Orangutan SVP and the onboard components

## Slide 44: Orangutan Controller Specifications

## Slide 45: Atmel Orangutan Programming
Atmel Studio Development Software
  Benefits of programming the Orangutan in C code
  APIs available for servos, LEDs, serial data, etc.

## Slide 46: Atmel Orangutan Programming
The Orangutan Robot Controller can control 8 servos using dedicated servo connections and programming APIs.

## Slide 47: Atmel Orangutan Programming
The Orangutan Robot Controller can control 8 more servos by allocating GPIO pins. This requires manual programming of the control signal, however.
Notes: Combine with previous slide

## Slide 48: Atmel Orangutan Programming

## Slide 49: Atmel Orangutan Programming

## Slide 50: Atmel Orangutan Programming

## Slide 51: Orangutan Implemented Functions

## Slide 52: Drumming State Machine Code Initial [0,9] byte Implemenation

## Slide 53: Robot Controller in Action

## Slide 54: Drumming State Machine Code Initial [0,9] byte Implementation

## Slide 55: Improved [a,z] byte Implementation

## Slide 56: Robot Controller States
The next slide shows the Byte Input from the host processor along with the outputs generated by the Robot Controller code:
S.M. (State Machine) Mode
Effective BPM
Delay Loop(ms) used to generate the desired BPM by the ration of [1/Delay(ms)]

## Slide 57
Byte Input | S.M. Mode | Effective BPM | Loop Delay(ms)
a | 1 | 60 | 500
b | 2 | 62 | 484
c | 3 | 65 | 462
d | 4 | 68 | 441
e | 5 | 70 | 429
f | 6 | 72 | 417
g | 7 | 75 | 400
h | 8 | 78 | 385
i | 9 | 80 | 375
j | 10 | 82 | 366
k | 11 | 85 | 353
l | 12 | 88 | 341
m | 13 | 90 | 333
n | 14 | 92 | 326
o | 15 | 95 | 316
p | 16 | 98 | 306
q | 17 | 100 | 300
r | 18 | 102 | 294
s | 19 | 105 | 286
t | 20 | 108 | 278
u | 21 | 110 | 273
v | 22 | 112 | 268
w | 23 | 115 | 261
x | 24 | 118 | 254
y | 25 | 120 | 250

## Slide 58: Robot Controller States
The next slide shows the Serial Module input from the host over the serial connection and button press
The Robot Controller uses a State Machine to determine the outputs at each BPM state:
  Delay(ms)
  Servo position
  LED on/off
  LCD screen text

## Slide 59: Partial sample of Robot Controller outputs

## Slide 60: Robot Controller States
As can be observed in the Left Servo column, the arm movement of up/down is randomly determined
During testing the monotonous sound of the drum beats was tiresome
Adding a random element to the one arm introduced a pleasing random pattern of drumbeats
Right arm is always in time with the calculated BPM and the left arm lends some character to the drumming pattern
Notes: Change back to bullet points DoNE

## Slide 61: Testing
Next we will look at the testing that was performed to assess the operation of the algorithm and improve the speed & accuracy of the results.

## Slide 62: Algorithm Testing
A series of ‘click tracks’ consisting of rhythmic pulses was created using Audacity
These files were used to test the accuracy of the host-side BPM Detection algorithm
Beat: | 35 BPM | 55 BPM | 60 BPM | 65 BPM | 70 BPM | 75 BPM | 80 BPM | 85 BPM
90 BPM | 95 BPM | 100 BPM | 105 BPM | 110 BPM | 115 BPM | 120 BPM | 125 BPM | 145 BPM
Notes: Insert example audio of click track DONE

## Slide 63: Algorithm Testing
The range of BPM Detection was set at 60-120 BPM. The click tracks included several files outside the range.
Beat: | 35 BPM | 55 BPM | 60 BPM | 65 BPM | 70 BPM | 75 BPM | 80 BPM | 85 BPM
90 BPM | 95 BPM | 100 BPM | 105 BPM | 110 BPM | 115 BPM | 120 BPM | 125 BPM | 145 BPM

## Slide 64: Algorithm Testing - Parameterization
A parameter set was used in 20 combinations to vary the values given to the algorithm. The results were calculated and graphed to determine calculation time and accuracy.
 | Range
Band Limits | None to [0 200 400 800 1600 3200]
Sample Rate | [2048, 4096, 8192, 16384]
Scaling | [0.75, 1.0, 1.25, 1.5]

## Slide 65: Algorithm Testing - Parameterization
Parameter values varied Band Limits, 4 different sample rates, and scaling factors added to the calculated results. Higher sample rates were more accurate but took longer to finish calculating.
 | Range
Band Limits | None to [0 200 400 800 1600 3200]
Sample Rate | [2048, 4096, 8192, 16384]
Scaling | [0.75, 1.0, 1.25, 1.5]

## Slide 66: Algorithm Testing – Time vs. Error
The input files for testing were of known BPM values. By varying the combinations of input parameters a range of results was obtained.
The goal was Time < 10s and Error < 10%
Error was calculated with this formula:

## Slide 67: Algorithm Testing – Time vs. Error
The results were graphed and examined
Chart: BPM Parameter Optimization: Time vs. Error
| 20.399999999999999 | 13.7 | 6.6 | 3 | 20.399999999999999 | 13.7 | 6.6 | 3 | 20.399999999999999 | 13.7 | 6.6 | 3 | 20.399999999999999 | 13.7 | 6.6 | 3 | 7.3 | 4.5 | 1.7 | 0.7
Error (%) | 4.6 | 6.48 | 17.96 | 18.64 | 29.55 | 17.95 | 8.25 | 10.98 | 16.53 | 10.2 | 7.7 | 10.1 | 1.67 | 5.14 | 6.18 | 5.65 | 2 | 4.51 | 6.37 | 8.77

## Slide 68: Algorithm Testing – Time vs. Error
Multiple results were within the goal
Chart: BPM Parameter Optimization: Time vs. Error
| 20.399999999999999 | 13.7 | 6.6 | 3 | 20.399999999999999 | 13.7 | 6.6 | 3 | 20.399999999999999 | 13.7 | 6.6 | 3 | 20.399999999999999 | 13.7 | 6.6 | 3 | 7.3 | 4.5 | 1.7 | 0.7
Error (%) | 4.6 | 6.48 | 17.96 | 18.64 | 29.55 | 17.95 | 8.25 | 10.98 | 16.53 | 10.2 | 7.7 | 10.1 | 1.67 | 5.14 | 6.18 | 5.65 | 2 | 4.51 | 6.37 | 8.77

## Slide 69: Algorithm Testing – Time vs. Error
One parameter set was within 5s and 5% error
Chart: BPM Parameter Optimization: Time vs. Error
| 20.399999999999999 | 13.7 | 6.6 | 3 | 20.399999999999999 | 13.7 | 6.6 | 3 | 20.399999999999999 | 13.7 | 6.6 | 3 | 20.399999999999999 | 13.7 | 6.6 | 3 | 7.3 | 4.5 | 1.7 | 0.7
Error (%) | 4.6 | 6.48 | 17.96 | 18.64 | 29.55 | 17.95 | 8.25 | 10.98 | 16.53 | 10.2 | 7.7 | 10.1 | 1.67 | 5.14 | 6.18 | 5.65 | 2 | 4.51 | 6.37 | 8.77

## Slide 70: Algorithm Testing – Time vs. Error
This result highlights 4.5 seconds calculation time and 4.51% average error for the BPM. This was well within our error and time goals.
(4.5s, 4.51%) | Values with best result of (Time, Error)
Band Limits | None to [0 200 400 800 1600 3200]
Sample Rate | [2048, 4096, 8192, 16384]
Scaling | [0.75, 1.0, 1.25, 1.5]

## Slide 71: Comparison with Rice team results (Error calculations added on right)
Song | Human-Detected Tempo (BPM) | Machine-Detected Tempo (BPM) | Error (%) 100*abs(expected -measured)/measured
Beverly Hills Cop Theme | 119 | 80.06 | 48.64
Lil Jon - Bia Bia | 78 | 59.51 | 31.07
Venga Boys - Boom | 139 | 140.16 | 0.83
Corelli | 91 | 185.98 | 2.14
Copland - Fanfare for the Common Man | 118 | 118.13 | 0.11
Green Acres Theme | 119 | 62.68 | 5.07
Stan Getz - Girl from Ipanema | 137 | 136.73 | 0.20
Will Smith - Getting Jiggy With It | 110 | 109.5 | 0.46
Jurassic Park Theme | 110 | 109.89 | 0.10
Green Day - Longview | 152 | 77.67 | 2.15
Limp Bizkit - Rollin' | 185 | 186.19 | 0.64

## Slide 72: Comparison with Rice team results (Error calculations added on right)
Song | Human-Detected Tempo (BPM) | Machine-Detected Tempo (BPM) | Error (%) 100*abs(expected -measured)/measured
Beverly Hills Cop Theme | 119 | 80.06 | 48.64
Lil Jon - Bia Bia | 78 | 59.51 | 31.07
Some of Rice’s calculations had an extremely high Error (%) while others were extremely low. Their implementation did not include parameterization of variables.

## Slide 73: Comparison with Rice team results
I was satisfied with the results by using the method of parameterization of results to find the best combination of Time and Error
Rice was not using the algorithm in a Real Time implementation as with the Drumming Robot
Rice project goals were therefore not likely to include optimizing for calculation time.
Next is a recap of media of the Drumming Robot in action.
Notes: More bullets

## Slide 74: Videos
Drumming Robot Media Recap
Drumming Robot Host Side
Drumming Robot Controller
Drumming Robot Full System
Heartbeat click track at 95BPM
Notes: Embed more drum videos

## Slide 75: Questions?

## Slide 76: References
Scheirer, Eric D. (1997). Tempo and beat analysis of acoustic musical signals. MIT Media Laboratory.
Cheng, Kileen; Nazer, Bobak; Uppuluri, Jyoti; Verret, Ryan (2001). Beat This – A Beat Synchronization Project. Rice University.
Handel, Stephen (1989). Listening. MIT Press.
Large, Edward W. and Kolen, John F. (1994). Resonance and the Perception of Musical Meter. Connection Science, Vol. 6, Nos. 2 & 3, p. 177.
Afonso, Valtino X.; Thompkins, Willis J.; Nguyen, Truong Q.; Luo, Shen (1999). ECG Beat Detection Using Filter Banks. IEEE Transactions on Biomedical Engineering, Vol. 46, No. 2.
Povel, Dirk-Jan and Essens, Peter (1985). Perception of Temporal Patterns. Music Perception: An Interdisciplinary Journal, Vol. 2, No. 4.
Jackson, Preston A.; Chan, Cy P.; Scalera, Jonathan E.; Rader, Charles M.; Vai, Michael (2004). A Systolic FFT Architecture for Real Time FPGA Systems. MIT Lincoln Laboratory.
Buso, Vincent (2012). VLSI Report. Illinois Institute of Technology.
Gerez, Sabih H. (2013). Hardware Implementations of the Fast Fourier Transform (FFT). University of Twente, The Netherlands.
Meyer-Baese, U. (2007). Digital Signal Processing with Field Programmable Gate Arrays. Springer.
Witte, Robert A. (2014). Spectrum and Network Measurements. SciTech.
Smith, Steven W. (2011). The Scientist and Engineer’s Guide to Digital Signal Processing. California Technical Publishing.
McKinney, Martin F. and Breebaart, Jeroen (2003). Features for Audio and Music Classification. Johns Hopkins University.
Lu, Li; Jiang, Hao; Zhang, HongJiang (2001). A Robust Audio Classification and Segmentation Method. ACM Multimedia.
O’Haver, Tom (2016). A Pragmatic Introduction to Signal Processing. University of Maryland at College Park.
Davies, Matthew E. P. and Plumbley, Mark D. (2006). A Spectral Difference Approach to Downbeat Extraction in Musical Audio. University of London Center for Digital Music.
Farid, Hany and Simoncelli, Eero P. (2004). Differentiation of Discrete Multi-Dimensional Signals. IEEE Transactions on Image Processing, Vol. 20, No. 20.