## Slide 1: Beat Extraction with Application to Robot Drumming
~
Michael Engstrom

## Slide 2: Beat Extraction Goals
Design a robot that will play drums in rhythm to an audio source which is detected in the environment
A robot control board will move servos to make arms and legs pound drums to a beat
An input device will detect the audio, extract the beat, and send the information to the robot controller

## Slide 3: Beat Extraction Phases
Software Design
  Input of audio source
  Beat detection
  Output to robot controller
Mechanical Design
  Arms and legs to beat drums
  Interface to control software

## Slide 4: Beat Detection
Tempo is complex

## Slide 5: Beat Detection
Tempo is complex
  Counterpoint, grouping, hierarchy are subtly combined and interpreted by the human ear

## Slide 6: Beat Detection
Tempo is complex
  Counterpoint, grouping, hierarchy are subtly combined and interpreted by the human ear
Beat (or pulse) is simpler

## Slide 7: Beat Detection
Tempo is complex
  Counterpoint, grouping, hierarchy are subtly combined and interpreted by the human ear
Beat (or pulse) is simpler
  The sense of equally spaced temporal units (Handel, 1989)

## Slide 8: Beat Detection
Tempo is complex
  Counterpoint, grouping, hierarchy are subtly combined and interpreted by the human ear
Beat (or pulse) is simpler
  The sense of equally spaced temporal units (Handel, 1989)
  Detection using frequency decomposition

## Slide 9: Beat Detection
Tempo is complex
  Counterpoint, grouping, hierarchy are subtly combined and interpreted by the human ear
Beat (or pulse) is simpler
  The sense of equally spaced temporal units (Handel, 1989)
  Detection using frequency decomposition
    Fourier Transforms can detect frequency power trends to determine the beat of an audio sample

## Slide 10: Beat Detection
Audio input samples can be decomposed
Algorithm steps:
  Frequency Filterbank
  Envelope Extraction (Fourier Transform)
  Differentiation
  Rectification
  Comb Filter (to match sample to known bpm)

## Slide 12: Beat Detection Algorithm
Step 1 – Frequency Filterbank

## Slide 13: Beat Detection Algorithm
Step 1 – Frequency Filterbank
  Split audio file into several frequency ranges
    Similar instrument ranges can inhibit the detection of the beat

## Slide 14: Beat Detection Algorithm
Step 1 – Frequency Filterbank
  Split audio file into several frequency ranges
    Similar instrument ranges can inhibit the detection of the beat
  Allows for different instruments to be detected
    0-200Hz, 200-400Hz, 400-800Hz, 800-1600Hz, 1600-3200Hz

## Slide 15: Beat Detection Algorithm
Step 1 – Frequency Filterbank
Each filter is implemented using a sixth-order elliptic filter

## Slide 16: Beat Detection Algorithm
Step 1 – Frequency Filterbank
Each filter is implemented using a sixth-order elliptic filter
  3 dB of ripple in the passband
  40 dB of rejection in the stopband.

## Slide 17: Beat Detection Algorithm
Step 1 – Frequency Filterbank

## Slide 18: Beat Detection Algorithm
Step 1 – Frequency Filterbank

## Slide 19: Beat Detection Algorithm
Step 2 – Envelope Extractor

## Slide 20: Beat Detection Algorithm
Step 2 – Envelope Extractor
  Filter each of the signal segments

## Slide 21: Beat Detection Algorithm
Step 2 – Envelope Extractor
  Filter each of the signal segments
    Convert to Frequency Domain using FFT or DFT

## Slide 22: Beat Detection Algorithm
Step 2 – Envelope Extractor
  Filter each of the signal segments
    Convert to Frequency Domain using FFT or DFT
    Convolve and transform signal

## Slide 23: Beat Detection Algorithm
Step 2 – Envelope Extractor
  Filter each of the signal segments
    Convert to Frequency Domain using FFT or DFT
    Convolve and transform signal
      Multiplication in Frequency Domain is the same as Convolution in the Time Domain

## Slide 24: Beat Detection Algorithm
Step 2 – Envelope Extractor
  Filter each of the signal segments
    Convert to Frequency Domain using FFT or DFT
    Convolve and transform signal
      Multiplication in Frequency Domain is the same as Convolution in the Time Domain
    Convert back to Time Domain

## Slide 25: Beat Detection Algorithm
Step 2 – Envelope Extractor: Example

## Slide 26: Beat Detection Algorithm
Step 2 – Envelope Extractor: Example

## Slide 27: Fourier Transforms
  Convert a signal from Time to Frequency Domain
    Separates frequency and magnitude components

## Slide 28: Fourier Transforms
  Convert a signal from Time to Frequency Domain
    Separates frequency and magnitude components
  Fourier Transform Pair:

## Slide 29: Fourier Transforms
  Convert a signal from Time to Frequency Domain
    Separates frequency and magnitude components
  Fourier Transform Pair:
  The Discrete Fourier Transform for digital signals:

## Slide 30: Beat Detection Algorithm
Step 3 – Differentiate signal
  Accentuate when the sound changes
  Corresponds to beats
Step 4 – Rectify signal
  Only see changes in sound
  Signals ready to be analyzed

## Slide 31: Beat Detection Algorithm

## Slide 32: Beat Detection Algorithm
Step 5 – Comb Filter
  Use various filters
  Determine which has highest energy
  Maximum value is the fundamental tempo

## Slide 33: Beat Detection Algorithm
A Comb Filter is used to find tempo maxima
  For delay T and gain α the magnitude response is

## Slide 34: Beat Detection Algorithm
A Comb Filter is used to find tempo maxima
  For delay T and gain α the magnitude response is
Local maxima are wherever is near 1
Key part of Beat Detection Algorithm

## Slide 35: Beat Detection Algorithm
Stimulate a comb filter with delay T and gain α with a right-sided pulse train of height A and period k
We get reinforcement (resonance) if T=k .
Let and be the input and output signals at time t
then = + (1-α)

## Slide 36: Beat Detection Algorithm

## Slide 37: Beat Detection Algorithm
Energy is higher at dominant tempos

## Slide 38: Software Design – Host Side
Matlab
  Input audio from file or microphone
    .wav file or 10 seconds of microphone sample
  Follow Handel Algorithm in Matlab
    Result is BPM value
  Send BPM control value using Serial connection to Robot Controller

## Slide 39: The ‘DIM’ Robot

## Slide 40: Robot Design
Mechanical
  Arms and legs to beat drums
    Using lamps, casters and servos
    3 degrees of freedom per arm
Software
  Pololu Robot Controller
    Interface to control software
      Input Serial BPM data
    Move robot limbs to drum at BPM

## Slide 41: Robot - Mechanical Design

## Slide 42: Robot - Mechanical Design
Added limbs to the DIM robot (as seen in the Robot Theater window)
Used servos to move limbs
A Pololu ‘Orangutan SVP’ robot controller handles the servo movement

## Slide 43: Robot - Mechanical Design
Arms
  Lamp arm from thrift store
  Servo moves arm indirectly

## Slide 44: Robot - Mechanical Design
Arms
  Shoulder made from caster wheel

## Slide 45: Robot - Mechanical Design
Arms
  Shoulder made from caster wheel

## Slide 46: Robot - Mechanical Design
Completed Arms
  Mounted on Robot torso

## Slide 47: Robot - Software Design
Serial interface to Orangutan board
  BPM and control information from Host

## Slide 48: Robot - Software Design
Serial interface to Orangutan board
  BPM and control information from Host
Output drumming movement in time with BPM
  Changes BPM of drumming every time new serial BPM data is received

## Slide 49: The Pololu Orangutan SVP Servo Controller

## Slide 50: Orangutan SVP from Pololu

## Slide 51: Orangutan Specifications

## Slide 52: Atmel Orangutan Programming
Atmel Studio Development Software
  Program the Orangutan in C code
    APIs available for servos, LEDs, serial data, etc.

## Slide 53: Atmel Orangutan Programming

## Slide 54: Atmel Orangutan Programming

## Slide 55: Atmel Orangutan Programming

## Slide 56: Orangutan Implemented Functions

## Slide 57: Drumming State Machine Code Initial [0,9] byte Implemenation

## Slide 58: Drumming State Machine Code Initial [0,9] byte Implemenation

## Slide 59: Drumming State Machine Code Improved [a,z] byte Implemenation

## Slide 60: Videos
Drumming Robot Video Examples
Drumming Robot Host Side
Drumming Robot Controller

## Slide 61: Questions?

## Slide 62: References
Scheirer, Eric D. (1997). Tempo and beat analysis of acoustic musical signals. MIT Media Laboratory.
Cheng, Kileen; Nazer, Bobak; Uppuluri, Jyoti; Verret, Ryan (2001). Beat This – A Beat Synchronization Project. Rice University.
Handel, Stephen (1989). Listening. MIT Press.
Large, Edward W. and Kolen, John F. (1994). Resonance and the Perception of Musical Meter. Connection Science, Vol. 6, Nos. 2 & 3, p. 177.
Afonso, Valtino X.; Thompkins, Willis J.; Nguyen, Truong Q.; Luo, Shen (1999). ECG Beat Detection Using Filter Banks. IEEE Transactions on Biomedical Engineering, Vol. 46, No. 2.
Povel, Dirk-Jan and Essens, Peter (1985). Perception of Temporal Patterns. Music Perception: An Interdisciplinary Journal, Vol. 2, No. 4.
Jackson, Preston A.; Chan, Cy P.; Scalera, Jonathan E.; Rader, Charles M.; Vai, Michael (2004). A Systolic FFT Architecture for Real Time FPGA Systems. MIT Lincoln Laboratory.
Buso, Vincent (2012). VLSI Report. Illinois Institute of Technology.
Gerez, Sabih H. (2013). Hardware Implementations of the Fast Fourier Transform (FFT). University of Twente, The Netherlands.
Meyer-Baese, U. (2007). Digital Signal Processing with Field Programmable Gate Arrays. Springer.
Witte, Robert A. (2014). Spectrum and Network Measurements. SciTech.
Smith, Steven W. (2011). The Scientist and Engineer’s Guide to Digital Signal Processing. California Technical Publishing.
McKinney, Martin F. and Breebaart, Jeroen (2003). Features for Audio and Music Classification. Johns Hopkins University.
Lu, Li; Jiang, Hao; Zhang, HongJiang (2001). A Robust Audio Classification and Segmentation Method. ACM Multimedia.
O’Haver, Tom (2016). A Pragmatic Introduction to Signal Processing. University of Maryland at College Park.
Davies, Matthew E. P. and Plumbley, Mark D. (2006). A Spectral Difference Approach to Downbeat Extraction in Musical Audio. University of London Center for Digital Music.
Farid, Hany and Simoncelli, Eero P. (2004). Differentiation of Discrete Multi-Dimensional Signals. IEEE Transactions on Image Processing, Vol. 20, No. 20.